## Slide 1: Statistical Considerations for Robust, Reproducible Biomarkers
11th EDRN Scientific Workshop
Pre-Workshop Meeting: Biomarkers and Regulatory Science

## Slide 2
Reproducible means that the same (or substantially similar) set of biomarker candidates are identified in multiple discovery experiments
A lab analyzes a set of case/control biospecimens with a methodology (e.g. mass spec for proteins, NGS for miRNAs) and identifies a set of candidate biomarkers
How do we know whether the candidate biomarkers are REPRODUCIBLE?
Complex dependence on:
  Size of candidate pool – 20,000+ proteins, 600 miRNAs
  Number of true biomarkers amongst candidates
  Sample size
  Separation of true biomarkers between cases and controls
  Biological variability of candidates between patients
  Measurement variability of repeated measurements
Simulation is one possible approach. Need hypothesis of how many true biomarkers there are and their distribution between cases and controls (separation, variability = biological + measurement).
Reproducible - Definition

## Slide 3
Robust means that biomarker candidate list remains the same (or substantially) similar despite small perturbations in:
Case and control populations (e.g. small changes in demographics)
Sample collection methods - does the patient have to sit still for 5 minutes before sample is obtained?
Processing procedures: e.g. labile plasma proteins prone to degradation within the protocol time frame from collection of blood to centrifugation to obtain plasma are NOT robust
Thawing of sample – if a smaller volume is required to measure candidates than stored volume
Storage conditions – More proteins intact over long term when samples stored in LN2 (-196 ℃) than at -80℃
Robust - Definition

## Slide 4: Three Topics (focus on statistical considerations)
At discovery stage (Phase 1) how to identify robust and reproducible biomarker candidates?
Effective triage process (Phase 2) leading to robust and reproducible biomarkers
Phase 3 Validation study for safety, effectiveness (FDA), clinical utility (CMS)

## Slide 5: At discovery stage (Phase 1) how to identify robust and reproducible biomarker candidates?
Discovery power
  discovery studies under powered
    miss good candidates
    false leads
Eliminate biases
  Matching on confounding factors (not just age/gender, e.g. blood collection setting and storage time)
  Lab procedure, blinding, randomization
  Early Detection: pre-diagnostic samples for discovery

## Slide 6: Effective triage process (Phase 2) leading to robust and reproducible biomarkers
Clinical application drives study design and everything else
  if not completely compliant, check possible biases that may cause
assay refinement as early as possible
  Major hurdle: $, infrastructure, incentive
early detection: test on pre-diagnostic samples before validation trial

## Slide 7: Clinical Validation Study (Phase 3) (safety and effectiveness)
Lock-down assay, final version
Cutoff: which option?
  Lock-down cutoff, or
  pre-specify desired sensitivity or specificity without lock-down cutoff
Collection and testing sites
Population heterogeneity
  Few collection sites from the target population
  Can training/test split in each collection site? NO
  Some collection sites for training, others collection sites for validation
  Testing sites (few testing sites, different lots, single site device)
  www.fda.gov/regulatory-information/search-fda-guidance-documents/design-considerations-pivotal-clinical-investigations-medical-devices

## Slide 8
Prospectively Obtained Samples
Pre-specified protocol for the clinical validation study (target population)
Inclusion/exclusion criteria
Samples/subjects are
from the target population of the IVD test
Measures of the clinical performance (e.g., clinical sensitivity, specificity, ..) are UNBIASED.
Time of testing: maybe be collected and tested
immediately (according to Instructions for Use)
stored prior to being tested (according to the claimed sample stability)
Selection of Samples for Clinical Validation Study

## Slide 9
Archived Samples
Without pre-specified protocol or/and
Protocol for different study
Additional Challenges
Samples may be non-representative of the target population (e.g, left-over of large tumors, no samples near the cutoff because of re-testing, not enough sample volume, …)
Inclusion of samples positive by another IVD test
Storage of samples (stability): especially challenging for new biomarkers; storage outside of the claimed sample stability
Selection of Samples for Clinical Validation Study

## Slide 10
If potentials for possible biases and stability issues are adequately addressed, archived samples can provide unbiased estimates of the performance and, therefore, can be used.
Early Detection: archived/prospectively collected samples
  Can archived samples be used for clinical validation study when clinical application uses fresh samples? YES
  If YES, what are required to do?
    Address possible biases
    Stability of samples!!! Changing storage conditions
    Bridging study between fresh and frozen samples
Clinical Validation Study (Phase 3)